# Environmental Isotopes
## Equilibrium fractionation
Equilibrium fractionation occurs in closed systems. Equilibrium fractionation of water during phase changes is mainly controlled by temperature. The initial isotopic ratio
of seawater is changed by a fractionation fator . This fractionation factor can be calculated using the empirical relationship
where , and are constants that are specific for each phase change, e.g. for water to vapour. The direction of the phase change is significant. The fractionation factor is defined as
In this case as
The term
is chosen, to produce values that can be read and interpreted more easily and as is quite close (within the error margin of the measurement) to for small deviations of the fractionation factor from 1.0 (or for small fractionations – which is very often the case in hydrology). Once the term has been calculated for a given phase change, it can be converted to . Finally, the isotope ratio of the resulting phase B can be calculated using the relationship
In hydrology, isotope ratios are given in permil as
Hence, once the isotope ratio has been calculated, it can be converted to a value using that relationship. Many values can be found at alphadelta
library(ggplot2) library(latex2exp) # Rs Seawater is the Standard for stable Isotope analysis of water # The ratios are given with their errors R18O = 2005.2E-6 R18Oe= 0.45E-6 R2H = 155.76E-6 R2He= 0.05E-6 d18Oe = 0.1 d2He = 1.0 # Majoube 18O/16O, equilibrium coefficients for water - vapour system D18O = 1.137 E18O = -0.42 F18O = -2.07 # 2H/H D2H = 24.844 E2H = -76.25 F2H = 52.61 # Temperature C & K - define a temperature range TC = seq(0,35,5) # Calculate equilibrium fractionation equilibrium <- function(TC){ # convert TC to TK TK <- TC*0 TK = TC+273.15 lnta18O = D18O*10^6/TK^2+E18O*10^3/TK+F18O lnta2H = D2H *10^6/TK^2+ E2H*10^3/TK+F2H lntas = data.frame(TC,TK,lnta18O,lnta2H) # ln(alpha)*1000 -> alpha alpha18O = exp(lnta18O/1000) alpha2H = exp(lnta2H/1000) lntas$alpha18O <- alpha18O lntas$alpha2H <- alpha2H # R(Start) -> R(Sample) S18O = R18O * alpha18O S2H = R2H * alpha2H lntas["S18O"] <- S18O # Add new column to data lntas["S2H"] <- S2H # Add new column to data # Rs -> delta d18O = (R18O- S18O) /R18O*1000 d2H = (R2H - S2H) / R2H*1000 lnta <- lntas # Replicate example data lntas <- cbind(lnta, d18O = d18O) # Add new column to data lnta <- lntas # Replicate example data lntas <- cbind(lnta, d2H = d2H) # Add new column to data return(lntas) } lntas <- equilibrium(TC) attach(lntas) ggplot(data=lntas, mapping=aes(x=TC, y=lnta18O)) + # ggtitle("Equilibrium fractionation of water") + geom_line(linetype="dashed", size = 0.5, color="blue") + geom_point(shape=21, fill="white", color="blue", size=3) + xlab("Temperature (Kelvin)") + ylab(TeX("$1000 \\cdot ln(\\alpha)$")) ggplot(data=lntas, mapping=aes(x=d18O, y=d2H)) + # ggtitle("Equilibrium fractionation of water") + geom_line(linetype="dashed", size = 0.5, color="blue") + geom_point(shape=21, fill="white", color="blue", size=3) + geom_errorbar(aes(ymin=(d2H-d2He), ymax=(d2H+d2He)), color="grey") + geom_errorbarh(aes(xmin = d18O-d18Oe, xmax = d18O+d18Oe), color="grey") + xlab(TeX("\\delta 18O $")) + ylab(TeX("\\delta 2H $")) + geom_text(label=TC, nudge_x=0.15, nudge_y=0.1, check_overlap=T)

If you do not have R or your computer or do not want to install it now, you can use the window below to run the code online. Just copy the R code in the (grey) block and insert it into the window. The example code can be deleted.
## Non-equilibrium fractionation
### Diffuse fractionation
Diffuse fractionation occurs, if a gas is moving through a vaccum or through another gas. A simpler case is given, if the gase travels through another inert gas. A more complex fractionation occurs, if the gas moves through another gase that contains the moving gas and that gets enriched with the moving gas during the process. This is the case, for example, when evaporation occurs over a water surface and changes the vapour content of the boundary layer during the process as a result of evaporation.
If the system is open, as during evaporation from a pond or during rainfall from a cloud, non-equilibrium fractionation occurs. There are different types of non-equilbrium fractionation. The first type is called diffuce fractionation. The basis for the calculation of diffuse fractionation effects is the difference in velocities of moving molecules. The water molecules with different isotopes having different masses, their velocities differ according to :
with the velocity of the molecule(s) in , the Boltzmann Konstant , the temperature in Kelvin and the mass of the molecule in kg. The fractionation can be derived from the ratio of velocities of different isotopes and is in proportion to
for vapour with a heavy isotope of oxygen and respectively for a heavy isotope of hydrogen:
It can be shown that for vapour moving through an inert gas such as e.g. dry air with a mas of 28.8 g per mol, the diffuse fractionation is in proportion to
in the case of water vapour containing a heavy isotope of oxygen and for vapour containing a heavy isotope of hydrogen instead:
This calculation shows, that oxygen isotopes fractionate more than hydrogen isotopes, a phenomenon commonly observed in evaporation of water from free surfaces.
However, as air usually contains vapour that has an isotopic composition as well and as the vapour in the air through which vapour diffuses interacts and exchanges with the vapour as well in terms of their isotopic composition, the fractionation of moist air is lower. Gonfiantini (1978) has suggested the empirical relationship:
Here, is the isotopic change resulting from the fractionation process with a fractionation factor of , hence
Inserting the densities for the different isotopic species of vapour with a heavy oxygen isotope and with a heavy hydrogen isotope, the empirical formulas for the isotopic change in permil read
and
In the case of evaporation from an open water surface, both effects combine and add up. The total fractionation at a temperature and at a humidity can be calculated as:
An application of this stepwise calculation indicates that the evaporation slope approaches the theoretical value for equilibration with increasing humidity. At the lowest possible humidity, the slope of the evaporation line is between 4.4 at lower temperatures and 3.4 at high temperatures in dry ambient air.
hum = 0.8 diffusefrac <- function(humidity = 0.8){ df18O = 14.2 df2H = 12.5 eps18 = df18O*(1-humidity) eps2H = df2H *(1-humidity) epsdf = data.frame(humidity, eps18, eps2H) return(epsdf) } epsdf <- diffusefrac(hum)

Both processes can be combined to obtain the isotopic fractionation during evaporation. At a given temperature a phase equilibrium between water and vapour will develop according to the equilibrium fractionation process. In addition, diffuse fractionation will conctribute additional fractionation by diffusion. The result of both processes results in isotope ratios of heavy and light oxygen and hydrogen isotopes in water that define the slope of the evaporation curve. For a given temperature and humidity, the combined effect of equilibrium and diffuse fractionation can now be calculated (still provided that sufficient water is available to prevent any fractionation effects due to enrichment in the reservoir of evaporating water).
### The Craig-Gordon Modell
### Rayleigh Fractionation
Rayleigh fractionation occurs, if a reservoir is depleted significantly. The initial istopic ratio changes towards the actual ratio at a certain degree of depletion if the fractionation factor for the depleting process is :
Code for Rayleigh fractionation. Please not that it requires the function equilibrium that is provided above. To run this code, you can add it to the first block of code at the bottom and execute the entire block - the function is then available.
alpha18O <- equilibrium(10)$alpha18O fR <- seq(0.9,1,0.001) R0 <- 2005.2E-6 R <- R0*fR^(alpha18O-1) plot(fR,R, type="l")