# Hydrochemistry of Seaswater Intrusion

TITLE Transport Example
SOLUTION 0 # Seawater
   units mmol/l
   pH 7.0
   pe 13.0 O2(g) -0.7
   Na 1.0 # Na has Retardation = 2
   Cl 1.0 # Cl has Retardation = 1, stagnant exchange
   N(5) 1.0 # NO3 is conservative
SOLUTION 1-100 # Fresh Groundwater
   units mmol/l
   pH 7.0
   pe 13.0 O2(g) -0.7
   K 1.0
   N(5) 1.0
EXCHANGE 1-10
    -equil 1
    X 1.e-2
TRANSPORT
   -cells 100
   -shifts 100
   -flow_direction forward
   -time_step 8640 # 1 day
   -boundary_conditions flux flux
   -lengths 100*10 # length of the box 10 m
   -dispersivities 100*0.1 # control the dispersion: v= 1m/day*10m
   -punch_cells 50 # cells to be written to selected output
   -punch_frequency 1-100 # time steps when results are written to s.o.
SELECTED_OUTPUT
        -file ex-transport_output.txt
        -temperature
        -pH
  -molalities H+ OH- Ca+2 K+ Na+ Cl- CO2 HCO3- CO3-2 CaX2 MgX2 NaX KX
        -saturation_indices	Calcite Gypsum Siderite
        -gases	CO2(g) N2(g)
END
TITLE Transport SOLUTION 0 # Seawater
  UNITS mmol/l
  Na 552.438
  K 12.021
  Ca 11.727
  Mg 61.304
  Cl 645.926
  S(6) 33.208
  C(+4) 2.835
  Br 0.813
  Sr 0.148
  Cd 1 charge
temp 25.0
EQUILIBRIUM_PHASES 0 SAVE SOLUTION 0 SOLUTION 1-100 # Groundwater
UNITS mmol/l
Cl 45.284
S(6)	0.688
C(+4) 3.684
Ca 12.6
Mg 4.480
Na 13.599
K 0.171
Sr 46.528
Cd 1 charge
temp 25.0
EXCHANGE 1-100
equil 1
X 1.e-2 TRANSPORT
1. cells 100
2. shifts 100
3. flow_direction forward
4. time_step 86400 # 1 day
5. boundary_conditions flux flux
6. lengths 100*10 # length of the box 10 m
7. dispersivities 100*0.1 # control the dispersion: v= 1m/day*10m
8. punch_cells 50 # cells to be written to selected output
9. punch_frequency 1-100 # time steps when results are written to s.o.
SELECTED_OUTPUT
1. file transport_c-1.txt
2. temperature
-molalities Ca+2 Mg+2 Na+ K+ HCO3- Cl- Br- SO4-2 Sr+2
1. saturation_indices Calcite Gypsum Siderite
2. gases CO2(g) N2(g)
END