# The impact of soil salinization on ground water chemistry (Zhang Luqianxue)
## Introduction
## Modeling
Code for rainwater evaporation
TITLE Rainwater evaporation from Ladouche2009
SOLUTION 1 Precipitation of rainfall in the South France
        units ueq/L
        pH 6.2
        Ca 163.3
        Mg 103.6
        Na 419.5
        K 13.9
        Cl 572.8
        C(4) 188.2	as HCO3 CO2(g) -2.2
        S(6) 98.5
        N(-3) 35.5
        N(5) 42.8
Br	0.195
  B	1.4616
  Sr	0.0286
  Se	1.963
EQUILIBRIUM_PHASES 1 Equilibrate with Minerals and gas
CO2(g)	-0.7 #change from -0.7 to -3.4
Calcite	0
SAVE solution 2
SELECTED_OUTPUT
-file	EvpRWLadouche2009.txt
-pH
-molalities	Ca+2 Mg+2 Na+ K+ Cl- SO4-2 NH4+ NO3- Br- H3BO3 Sr+2 HSeO3- SeO3-2 HCO3- CO3-2
-saturation_indices	Calcite Gypsum Epsomite
END
TITLE Evaprate water
USE solution 2
REACTION 1 evaporation
H2O	-1.0
5.55 11.11 16.67 22.22 27.78 33.33 38.89 44.44 50.0 51.0 52.0 53.0 54.0 55.0 55.1 55.2 55.3 55.4 55.41 55.42 55.43 55.44 55.45 55.46 55.47 55.48 55.49 55.5 moles
SAVE solution 3
code for irrigation water evaporation
TITLE Irrigation water evaporation from Galazoulas2014
SOLUTION 1 Precipitation of rainfall in the Greece
        units mg/L
temp	22.4
       pH 7.1
        Ca 513.2
        Mg 140.5
        Na 279.1
        K 4.1
        Cl 1619
        C(4) 198	as HCO3
        S(6) 129.5
N(5)	1.2
Sr	2.3571
As	0.0055
Co	0.0005 charge
Cr	0.0245
Li	0.0219
Mn	0.0023
Zn	0.1871
Se	0.0168
Ni	0.003
Fe	1.6406
EQUILIBRIUM_PHASES 1 Equilibrate with Minerals and gas
CO2(g)	-0.7
Calcite	0
SAVE solution 2
SELECTED_OUTPUT
-file	Openme.txt
-pH
-molalities	Ca+2 Mg+2 Na+ K+ Cl- SO4-2 NH4+ NO3- Br- H3BO3 Sr+2 HSeO3- SeO3-2 HCO3- CO3-2 HAsO4-2 H2AsO4- Co+2 Cr(OH)2+ Cr(OH)+2 Cr(OH)3 Fe+2 FeSO4 Fe(OH)2+ Fe(OH)3 Fe(OH)4- Li+ Mn+2 Ni+2 HSeO3- Sr+2 Zn+2
-saturation_indices	Calcite Gypsum Epsomite
END
TITLE Evaprate water
USE solution 2
REACTION 1 evaporation
H2O	-1.0
5.55 11.11 16.67 22.22 27.78 33.33 38.89 44.44 50 51 52 53 54 55 55.1 55.2 55.3 55.31 55.32 55.33 55.34 55.35 55.36 55.37 55.38 55.39 55.4 moles
SAVE solution 3
## Result
Rainwater：comparisontraceladouche2009.xlsx
Irrigation water：comparisontracegalazoulas2014.xlsx
raw data:tracegalazoulas2014.xlsx
Source:galazoulas2014.pdf
Structure：